Polymer in confined space : MC simulation (Minor project)

Input data structures

- int : Number of monomers
- float : bond length
- float : bond diameter
- float : slab thickness
- int : number of conformations wanted
- bool : volume exclusion
- float : minimal correlation threshold
- string : type of collisions detector

Output data
For each accepted conformation (uncorrelated)
  - end-to-end distance
  - gyroradius
  - full conformation (position of each monomer)
  - number of pivoting attemps
  - number of accepted pivoting
  - number of monomers moves

For each accepted polymer move
  - auto-correlation

1. Overall algorithm

   currentPolyer , oldPolymer = generateStartingConformation()
  For i=1 to Nconformations
   |	Do
   |	|	collisions=False
  |	|	nextPolymer=currentPolymer
  |	|	Mp = selectMonmerAsPivot(nextPolymer)
   |	|	nextPolymer = proposeMove(moveType,Mp)
  |	|
  |	|	collisions= checkGeometryCollision(nextPolymer, geometry)
  |	|	If SAW:
  |	|	collisions+= checkVolumeExclusion(nextPolymer)
  |	|
  |	|	If not collisions
  |	|	currentPolymer = nextPolymer
  |	|
  |	While collisions = True OR correlations(currentPolymer, oldPolymer) >minCorrelations
  |	saveConformation(curentPolymer)
  |	oldPolymer=currentPolymer
  End For
2. Detailed algorithm : With plane pivot method
   Version 1 : First move then check collisions
   currentPolyer = oldPolymer = generateStartingConformation()
  For i=1 to Nconformations
  |	Do
  |	|	collisions=False
  |	|	nextPolymer=currentPolymer
  |	|	Mp = selectMonmerAsPivot(nextPolymer)
  |	|	theta = generatePivotAngle()
  |	|	For j=p+1 to N
  |	|	|	deltaZ=generateRandomDeltaZ()
  |	|	|	displaceMonomer(Mj,deltaZ) // displace along axis, respect lenght
  |	|	|	pivotMonomer(Mj,theta)
  |	|	End For
  |	|
  |	|	collisions= checkGeometryCollision(nextPolymer, geometry)
  |	|	If SAW:
  |	|	collisions+= checkVolumeExclusion(nextPolymer)
  |	|
  |	|	If not collisions
  |	|	currentPolymer = nextPolymer
  |	|
  |	While collisions = True OR correlations(currentPolymer, oldPolymer) >minCorrelations
  |	saveConformation(curentPolymer)
  |	oldPolymer=currentPolymer
  End For

  Version 2 : Check collisions with slab after each monomer move
  currentPolyer = oldPolymer = generateStartingConformation()
  For i=1 to Nconformations
  |	Do
  |	|	collisions=False
  |	|	nextPolymer=currentPolymer
  |	|	Mp = selectMonmerAsPivot(nextPolymer)
  |	|	theta = generatePivotAngle()
  |	|	For j=p+1 to N
  |	|	|	deltaZ=generateRandomDeltaZ()
  |	|	|	displaceMonomer(Mj,deltaZ) // displace along axis, respect lenght
  |	|	|	pivotMonomer(Mj,theta)
  |	|	|	collisions= checkGeometryCollision(Mj,geometry) //break if collisions
  |	|	End For
  |	|
  |	|	If SAW:
  |	|	collisions+=checkVolumeExclusion(nextPolymer)
  |	|
  |	|	If not collisions
  |	|	currentPolymer = nextPolymer
  |	|
  |	While collisions = True OR correlations(currentPolymer, oldPolymer) >minCorrelations
  |	saveConformation(curentPolymer)
  |	oldPolymer=currentPolymer
  End For